## Slide 1
HARDWARE · NUMERICAL LINEAR ALGEBRA
A Fixed-Point Gram–Schmidt
QR Decomposition Engine
Synthesisable Verilog-2001 · Modified Gram–Schmidt · Fully parameterised
8
RTL modules
23/23
regression configs
2P+1
multipliers
1.13
ulp worst rsqrt error
A = Q · R
Notes: Goal of the deck: start from what QR decomposition is, why it matters, then move gradually into the fixed-point hardware design and the Verilog files that implement it.

## Slide 2
THE BASICS
One matrix, factored into two useful ones
A (M×N)
=
Q (M×N)
×
R (N×N)
zeros
non-zero
Q is orthonormal
Every column has unit length and is perpendicular to every other. Formally QᵀQ = I.
R is upper triangular
Everything below the diagonal is exactly zero, so systems in R solve by back-substitution.
Why factor at all?
Solving with A directly squares the condition number. Solving with Q and R does not — the error stays proportional to κ(A).
Orthonormal columns are numerically precious: they never amplify error.
That is the whole reason QR exists.
This engine computes the thin QR decomposition, with M ≥ N.
Notes: A is the input. Q holds the orthonormalised directions, R holds the coefficients that rebuild A from them.

## Slide 3
MOTIVATION
Why a hardware QR engine is worth building
1
MIMO wireless
Detection and precoding in 5G need QR of the channel matrix every coherence interval — thousands of times a second.
2
Adaptive beamforming
Radar and array processing solve constrained least-squares continuously, in real time.
3
Kalman filtering
Square-root filters propagate a triangular factor instead of the covariance, staying stable.
4
Least squares
min ‖Ax − b‖ becomes Rx = Qᵀb — a triangular solve, no normal equations, no squared condition number.
Common thread: the same decomposition, repeated at high rate, with a hard latency budget — exactly the case where a CPU or DSP stops being enough.
Notes: Software QR is fine for one-off computation. Hardware pays off when the decomposition is on the critical path of a streaming system.

## Slide 4
THE ALGORITHM
Gram–Schmidt: remove what you already have
q₀
a₁
(q₀·a₁) q₀
v = a₁ − projection
⌐
The residual is perpendicular to q₀ by construction. Normalise it and it becomes q₁.
Repeat for every column
1
Measure
R[j][j] = ‖v_j‖
2
Normalise
q_j = v_j · (1/‖v_j‖)
3
Project
R[j][k] = q_j · v_k
4
Subtract
v_k = v_k − R[j][k]·q_j
Four phases, and every one is either a dot product or a vector scaled by a scalar — two operations the hardware has to be good at.
Notes: The entire algorithm reduces to two primitives. That is what makes it a good fit for a small fixed datapath.

## Slide 5
THE KEY DECISION
Classical vs Modified Gram–Schmidt
Classical Gram–Schmidt
v = a_k − Σ (q_j · a_k) q_j
Every projection is measured against the ORIGINAL column. Errors already sitting in q_j are never observed again, so they simply pile up.
Modified Gram–Schmidt
v = a_k
for j < k: v ← v − (q_j · v) q_j
Each projection is measured against the RUNNING residual, so an error in q_j is partly cancelled by the projections that follow it.
Loss of orthogonality ∝ u · κ(A)²
At κ = 10³ that is roughly 5×10⁵ LSB — past full scale. Nothing usable comes out.
Loss of orthogonality ∝ u · κ(A)
Measured on this hardware at κ = 10³: 102 LSB. The squared term is gone.
The price of MGS is a sequential inner loop — the next coefficient cannot be computed until the previous update lands. This design pays it, and buys throughput back with lane parallelism instead.
Notes: This is the single most important decision in the project. In floating point the difference is academic; in 18-bit fixed point it decides whether the core works at all.

## Slide 6
PART TWO
From mathematics
to silicon
What changes when the numbers stop being real, and start being 18 bits wide.
Notes: Transition slide: the algorithm is settled, now the implementation constraints take over.

## Slide 7
NUMBER REPRESENTATION
Fixed point: an integer with an agreed binary point
s
2⁰
2⁻¹ 2⁻² 2⁻³ ··· 2⁻¹⁶
↑ binary point
W = 18 bits total, F = 16 fractional → Q2.16
Stored as
a plain two's-complement integer x · 2¹⁶
Range
−2 to +1.99998
Resolution
2⁻¹⁶ ≈ 0.0000153 (one LSB)
Hardware cost
an ordinary integer multiplier — no exponent logic
Why not floating point?
Area
A float multiplier costs several times an integer one, plus normalisation and rounding logic.
Timing
Exponent handling adds pipeline depth that a streaming core pays for on every operation.
Predictability
Fixed point has one uniform LSB. Error analysis becomes arithmetic, not statistics.
The catch: fixed point has no automatic scaling. Every range decision becomes the designer's responsibility.
Notes: Fixed point trades automatic range handling for area and predictability. The next slide is the contract that buys back safety.

## Slide 8
THE FIXED-POINT CONTRACT
One input rule keeps the entire datapath in range
Scale A so that every column satisfies ‖a_j‖ < 2. A sufficient condition is |a_ij| ≤ 1/√M.
‖a_j‖ < 2
the input rule
‖v‖ ≤ ‖a_j‖
residuals only shrink
|r_kj| ≤ ‖a_j‖
R is bounded too
|q_ij| ≤ 1
Q is always representable
Because Q is orthonormal by construction, its entries can never exceed 1 — so bounding the input bounds everything downstream.
Signal
Format
Meaning
A, V, Q, R
Q2.16
the datapath word, W = 18 bits
dot accumulator
Q16.32
48 bits — every partial sum exact
1/‖v‖ and ‖v‖
Q12.20
scalars, range ±2048
rsqrt mantissa
Q2.30
internal, normalised to [1,4)
Violations saturate rather than wrap, and raise the sticky ovf_flag output — the core never silently produces nonsense.
Notes: A single scaling condition on the input guarantees the whole pipeline. Guard bits in the accumulator do the rest.

## Slide 9
THE ENGINE
Top-level architecture
A stream in
column-major
M·N beats
Vector RAM
ram_2r1w
2 read · 1 write
width P·W depth (M/P)·N
holds A → V → Q in place
port A
port B
vec_mac
P mults + adder tree
exact ACC_W accumulator
vec_axpy
P mults
scale · scale-and-subtract
rsqrt_unit
Newton–Raphson
ONE shared 34×34 multiplier
1/‖v‖ scalar
R RAM
ram_1r1w N·N words
‖v‖ → R[j][j]
R[j][k]
write-back, in place
Q out
column-major M·N
R out
row-major N²
Control
FSM
gs_top
15 states
address gen
write-addr
delay line
stream
handshakes
start · busy · done · rank_def · ovf_flag
Notes: One memory, two arithmetic blocks, one reciprocal-sqrt unit, one FSM. Everything else is addressing.

## Slide 10
DATAFLOW
One column, five phases, shared hardware
NORM
‖v_j‖²
stream v_j through vec_mac,
accumulate exactly in 48 bits
RSQ
1/‖v_j‖ and ‖v_j‖
one rsqrt_unit call
writes R[j][j]
SCALE
q_j = v_j · (1/‖v_j‖)
vec_axpy in normalise mode,
in place
PROJ
R[j][k] = q_j · v_k
vec_mac again,
for every later column k
UPD
v_k −= R[j][k] · q_j
vec_axpy in subtract mode,
in place
repeat for every remaining column k
Note what is reused: NORM and PROJ are the same vec_mac. SCALE and UPD are the same vec_axpy, differing only by one control bit. Two multiplier arrays cover four of the five phases.
Notes: Column j is normalised, then its projection is removed from every column to its right, before moving to column j+1.

## Slide 11
VEC_AXPY.V
Design decision 1 — one multiplier array, two jobs
Normalisation and projection removal are both “a vector times a scalar”. They are never active in the same cycle, so one array of P multipliers serves both.
use_dst = 0
NORMALISE
dst = sat_round(src · scalar)
use_dst = 1
PROJECT
dst = dst_in − sat_round(src · scalar)
// stage 1 : P multipliers, shared by both modes
for (i = 0; i < P; i = i + 1)
prod[i] <= $signed(src[i*W +: W]) * scalar;
// stage 2 : requantise, optionally subtract, saturate
round_sat #(.IN_W(PW), .OUT_W(W), .SHIFT(SC_F)) u_rs (...);
wire signed [W:0] diff = $signed(dst_r[g*W +: W])
- $signed({t[W-1], t});
dst_o[i*W +: W] <= use_r ? s_flat[...] // PROJECT
: t_flat[...]; // NORMALISE
What this buys
Half the DSPs on the update path
One array instead of two, for the entire projection-removal pipeline.
A single rounding policy
Both modes go through the same round_sat, so the error model has one entry, not two.
Saturation, never wraparound
Overflow clamps to ±max and raises a flag; a wrapped value would look plausible and be catastrophic.
Notes: The mode bit is the only structural difference between normalisation and projection removal.

## Slide 12
RSQRT_UNIT.V
Design decision 2 — no divider, no square root
The algorithm needs two things
1 / ‖v‖ to normalise the column ‖v‖ to store as R[j][j]
The naive answer
Instantiate a square-root block AND a divider. Two large, slow, awkward units — for one scalar per column.
‖v‖ = m · ( 1 / √m ) · 2ʰ
Because m / √m = √m, the reciprocal square root already contains the square root — one extra multiply recovers it.
1
multiplier
one 34×34, reused by every Newton–Raphson step and by the square-root recovery
0
dividers
the reciprocal falls out of the iteration itself — division never appears
0
sqrt blocks
the norm is recovered from a value the unit has already computed
Verified over 616 directed tests: worst error 1.129 ulp on 1/√x and 0.500 ulp on √x, latency 24 cycles.
Notes: This is the trick that keeps the whole engine small. A divider would have dominated both area and critical path.

## Slide 13
RSQRT_UNIT.V
Inside the reciprocal square root
1
Normalise
reduce ‖v‖² to m·2³⁰ with m ∈ [1,4)
and an even exponent e; h = e/2
2
Seed
64-entry Q1.15 ROM gives ≈ 6 correct bits
(worst seed error 0.01526)
3
Iterate
y ← y (3 − m y²) / 2, NR_ITER = 3
each pass doubles the correct bits
4
Recover
√m = m·y, then denormalise both
outputs by 2ʰ
S_MUL1: t1 = y*y >> MF
S_MUL2: t3 = 3 - m*t1
S_MUL3: y = y*t3 >> (MF+1)
iter <- iter + 1
st <- (iter == NR_ITER-1)
? S_SQRT : S_MUL1;
S_SQRT: ma <- Mm; mb <- Yv; // m * y
pr <- pmul; // = sqrt(m)
One multiplier, sequenced
A phase bit registers the operands on one edge and captures the product on the next, placing flip-flops on both sides of the multiplier. Three multiplies per iteration are folded onto the same 34×34 array, so more iterations cost cycles — never area.
Newton–Raphson converges quadratically: 6 seed bits → 12 → 24 → beyond the 20 fractional bits the output format carries.
Notes: The unit runs once per column, so its 24-cycle latency is negligible against the streaming phases.

## Slide 14
GS_TOP.V
Design decision 3 — update in place
a_j
the input column
v_j
the running residual
q_j
the final unit vector
one memory slot,
three lifetimes
No second matrix buffer — which halves the memory relative to a source-and-destination design.
The write-address delay line
read addr
issued
RAM
+1 cycle
vec_axpy
+2 cycles
write addr
wa1→wa2→wa3
A result must land in exactly the slot it came from. Three cycles of latency means three registers of address delay — derived from the same constants that define the module latencies, never hard-coded.
Why this is the classic bug
An off-by-one here does not crash. It writes each updated element one slot away from where it belongs, and the decomposition quietly returns a wrong answer that still looks like a matrix.
That is why the depth is computed from DRAIN and the module latencies, and why the testbench checks every output word against a bit-accurate model rather than a tolerance.
Elaboration-time checks enforce M % P == 0 and N ≤ M.
Notes: In-place update is what keeps the memory small; the delay line is the price, and it must be exact.

## Slide 15
GS_TOP.V
The control FSM — 15 states
ST_IDLE
wait start
ST_RCLR
zero R
ST_LOAD
M·N beats
for each column j = 0 … N−1
ST_NORM
‖v‖²
ST_NORM_D
drain
ST_RSQ
1/‖v‖, ‖v‖
ST_SCALE
q_j
ST_SCALE_D
drain
for k = j+1 … N−1
ST_PROJ
ST_PROJ_D
ST_UPD
ST_UPD_D
ST_OUTQ
Q col-major
ST_OUTR
R row-major
ST_FIN
done pulse
Why the _D states exist
Each arithmetic block has pipeline latency. After the last element is issued, the FSM must wait DRAIN = 6 cycles for the result to emerge before acting on it. Rather than hide this in counters, each streaming phase has an explicit drain state — the latency becomes visible in the state diagram instead of buried in control logic.
R is zeroed first, in ST_RCLR
so the strict lower triangle streams out as exact zeros with no special-case logic at the output port.
Notes: Back-to-back decompositions need no reset; the testbench asserts two consecutive runs are identical.

## Slide 16
PART THREE
The repository
Eight RTL modules, a bit-accurate model, two testbenches, and the regression that found the bugs.
Notes: Now the concrete files.

## Slide 17
WHAT IS IN THE BOX
Repository map
rtl/
synthesisable Verilog-2001
gs_top.v
616
FSM, addressing, R memory, stream ports
vec_mac.v
81
P-lane dot product, exact accumulation
vec_axpy.v
107
P-lane scale / scale-and-subtract
rsqrt_unit.v
244
Newton–Raphson, returns 1/‖v‖ and ‖v‖
rsqrt_seed_rom.v
90
64×16 seed table (generated)
round_sat.v
43
round-half-up + signed saturate
ram_2r1w.v
56
vector memory, mirrored banks
ram_1r1w.v
29
R matrix memory
model/
the golden reference
gs_model.py
249
bit-accurate model — the source of truth
gen_stimulus.py
145
stimulus + expected output, 6 cases
check_qr.py
127
independent numpy verification
gen_seed_rom.py
94
regenerates the seed ROM
tb/ · sim/ · syn/ · docs/
verification and build
tb_gs_top.v
315
self-checking, random stalls
tb_rsqrt.v
175
616 directed tests
regress.py
163
23-configuration sweep
Makefile
73
test · rsqrt · lint · regress
synth_vivado.tcl
—
out-of-context synthesis + reports
docs/*.md
359
architecture and fixed-point analysis
≈ 2,600 lines total · MIT licensed · CI runs the model self-test, the seed-ROM reproducibility check, lint, Yosys elaboration and the full regression on every push.
Notes: Line counts are real. gs_top is the biggest file because it holds all the addressing and the FSM.

## Slide 18
gs_top.v
Parameters and ports
module gs_top #(
parameter integer M = 8, // rows
parameter integer N = 4, // columns, N <= M
parameter integer P = 2, // lanes, M % P == 0
parameter integer W = 18, // datapath word
parameter integer F = 16, // fractional bits
parameter integer ACC_W = 48, // >= 2W + log2(M)
parameter integer SC_W = 32, // scalar width
parameter integer SC_F = 20, // scalar fraction
parameter integer NR_ITER = 3,
parameter integer EPS_SHIFT = 2*F - 2*(SC_W-1-SC_F)
)(
input wire clk, rst_n,
input wire start,
output reg busy, done,
output reg rank_def, // sticky
output reg ovf_flag, // sticky
input wire [W-1:0] s_a_tdata, // A, column-major
input wire s_a_tvalid,
output wire s_a_tready,
output wire [W-1:0] m_q_tdata, // Q, column-major
output wire [W-1:0] m_r_tdata // R, row-major
);
Everything is a parameter
Geometry, word width, lane count and iteration count are all elaboration-time. Nothing is hard-coded to the 8×4 default.
EPS_SHIFT is derived, not chosen
The rank-deficiency threshold is computed from the scalar format, so the two can never drift apart. More on this later.
AXI-Stream style throughout
tdata / tvalid / tready on all three data ports, transfer on the rising edge when both are high.
Sticky status flags
rank_def and ovf_flag latch for the whole decomposition — the core reports trouble rather than hiding it.
M % P == 0 and N <= M are checked at elaboration time and fail the build loudly.
Notes: The parameter list is the whole configuration surface of the core.

## Slide 19
vec_mac.v
The dot product, with no intermediate rounding
// stage 1 : P parallel multipliers
for (i = 0; i < P; i = i + 1)
prod[i] <= $signed(a[i*W +: W])
* $signed(b[i*W +: W]);
// stage 2 : adder tree, sign-extended to ACC_W
always @* begin
sum_c = {ACC_W{1'b0}};
for (i = 0; i < P; i = i + 1)
sum_c = sum_c
+ {{(ACC_W-PW){prod[i][PW-1]}}, prod[i]};
end
// stage 3 : running accumulator, ACC_W = 48 bits
if (clr) acc <= {ACC_W{1'b0}};
else if (v2) acc <= acc + sum2;
Why 48 bits
ACC_W ≥ 2·W + ⌈log₂ M⌉
Each product of two Q2.16 values is Q4.32. Summing M of them needs log₂M more bits of headroom. At W=18, M=64 that is 42 — so 48 leaves margin all the way to M = 4096.
The payoff
Because the accumulator holds every partial sum exactly, a dot product rounds exactly once — when the final result is written back.
A design that rounded after each MAC would inject M independent errors into every projection coefficient, and MGS would lose the accuracy it was chosen for.
Three pipeline stages: multiply → adder tree → accumulate. Latency 3 cycles from en to acc.
Notes: Guard bits are cheap in an accumulator and expensive to do without.

## Slide 20
model/gs_model.py
The golden model reproduces the hardware bit for bit
def rnd_sat(x, shift, w):
"""round-half-up then saturate - matches round_sat.v"""
y = (x + (1 << (shift - 1))) >> shift
return sat(y, w)
def mgs_fixed(A, W=18, F=16, ...):
for j in range(N):
n2 = sum(v[i][j] * v[i][j] for i in range(M))
if n2 < EPS_NORM2: # cannot normalise
rank_def = True # -> R[j][j] = 0, q_j = 0
continue
y, s = rsqrt_fx(n2) # same seed ROM, same NR
for i in range(M):
v[i][j] = rnd_sat(v[i][j] * y, SC_F, W)
for k in range(j + 1, N):
r = rnd_sat(dot(v[:,j], v[:,k]), F, W)
for i in range(M):
v[i][k] -= rnd_sat(v[i][j] * r, F, W)
Integer arithmetic only
No floats anywhere in the model — every value is the same integer the RTL registers hold.
Same rounding, same saturation
rnd_sat mirrors round_sat.v exactly, including the half-up bias.
Same seed table, same iterations
rsqrt_fx walks the identical 64-entry ROM and the identical three Newton steps.
Exact equality, not tolerance
The testbench asserts every output word matches. A tolerance check would hide the very bugs this is built to catch.
Simplified for the slide — the real model also tracks the overflow flag and the full rsqrt normalisation.
Notes: A bit-accurate model is what turns 'looks about right' into a pass/fail signal.

## Slide 21
HOW IT IS CHECKED
Verification: three layers that fail in different ways
1
Bit-exact model match
Every Q and R word must equal the golden model exactly.
Catches: addressing errors, off-by-one delay lines, control bugs, rounding differences.
2
Independent numpy check
check_qr.py recomputes A−QR, QᵀQ−I, triangularity and diagonal sign from the raw output.
Catches: cases where RTL and model agree but both are wrong — a shared design mistake.
3
Directed unit tests
616 rsqrt vectors across 13 octaves; lint; Yosys elaboration with check -assert.
Catches: numerical corner cases, inferred latches, multiply-driven nets.
Also asserted
✓
exact beat counts on all three streams
✓
R strictly upper triangular
✓
non-negative R diagonal
✓
two back-to-back runs identical
✓
random input bubbles tolerated
✓
random output backpressure tolerated
✓
seed ROM regenerates byte-identical
Layer 2 is the one that matters most: bit-exactness proves the hardware matches the intent, but it cannot tell you the intent was wrong.
Notes: Each layer catches a class the others cannot. That separation is what made the scalar-saturation bug findable.

## Slide 22
RESULTS
Regression results — 23 of 23 configurations pass
case
matrix
lanes
orthogonality error
result
random
8×4 … 64×16
P = 1,2,4,8
1.4 – 4.6 LSB
✓ pass
illcond
κ(A) = 1.0×10³
P = 2,4
79 – 102 LSB
✓ pass
extreme
κ(A) ≈ 2×10⁵
P = 2,4
flags rank_def
✓ pass
rankdef
duplicated column
P = 2
flags rank_def
✓ pass
identity
κ(A) = 1
P = 2
0.0 LSB
✓ pass
hadamard
κ(A) = 1
P = 2
2.7 LSB
✓ pass
Every case matched the model exactly
Word for word, including the failing configurations before they were fixed — which is precisely how the scalar-saturation bug was isolated to the format rather than the logic.
Measured against theory
MGS predicts ≈ κ/2 LSB of orthogonality loss. At κ = 10³ that bound is 500 LSB; the hardware measures 102. The results sit at or below the bound across four orders of magnitude.
Notes: Coverage spans lane counts, geometries including N=1 and M=N, and all six matrix cases.

## Slide 23
WHAT WENT WRONG
Three bugs the regression caught
1
Lane counters sized wrong
pack_cnt and out_el were sized from the chunk count M/P instead of the lane count P. Whenever P exceeded M/P the counter could not reach P−1.
Symptom: hung forever in ST_LOAD at M=8, P=8.
Fix: a separate LCW = clog2(P+1) width for lane counters.
2
Scalar saturation, silently
1/‖v‖ was Q8.24, saturating at 128. Ill-conditioned input drove residual norms to 0.002, needing a factor of 455.
Symptom: a confident, plausible, wrong Q — and the model agreed, because it shared the format.
Fix: widen to Q12.20 and derive the rank threshold from the saturation point.
3
Two testbench defects
$itor truncates to 32 bits, mislabelling a 1.25 input as 0.25. And the AXI handshake was sampled on the wrong clock edge.
Symptom: two 'RTL failures' where the RTL was correct all along.
Fix: 16-bit-limbed conversion; drive and sample on posedge. Both are commented at the point they bit.
The middle one is the lesson: bit-exactness against a reference proves the hardware matches the intent. It cannot tell you the intent was wrong — only the independent check could.
Notes: Worth being candid that two of the early failures were testbench defects, not RTL defects.

## Slide 24
THROUGHPUT AND AREA
Performance — a cycle model that is exact
cycles = (M/P + 6)·N·(N+1) + 26·N + 3·(M/P)·N + 2·M·N + 5·N² + 1
Chart: Measured cycles per decomposition
| 8×4 P=1 | 8×4 P=2 | 8×4 P=4 | 8×4 P=8 | 16×8 P=4 | 64×8 P=8 | 64×16 P=8
cycles | 625 | 497 | 433 | 401 | 1601 | 2753 | 7937
Exact at all nine points
Predicted equals measured with no fitting, from 8×4 up to 64×16. The formula is a design tool, not an estimate.
Where P pays off
At 8×4, going P=1 → P=8 buys only 1.6× — streaming and rsqrt overheads dominate. Lanes pay off for tall matrices, where M/P is the leading term.
Multiplier count is exactly 2P + 1, confirmed by Yosys cell counts. On Xilinx, roughly 3P + 4 DSP48E1.
Notes: Cycle counts measured with no back-pressure, using the -DGS_NOSTALL testbench option.

## Slide 25
WHAT THIS DOES NOT DO
Honest limits
!
Conditioning ceiling
Useful accuracy needs κ(A) below roughly 4×10³ at default parameters. Beyond that the engine raises rank_def and zeroes the column — deliberately, rather than emitting a plausible wrong answer.
!
Input scaling is the user's job
Fixed point has no automatic exponent. Columns must be scaled to ‖a_j‖ < 2 before they arrive.
!
Synthesis is elaboration-checked only
Yosys passes cleanly with no latches or multiply-driven nets. But Yosys is not Vivado — the 3P+4 DSP estimate and the ~166 MHz target in gs.xdc are informed projections, not measured results. Run the Vivado script on the real part before trusting either.
!
MGS, not Householder
For unconditional backward stability with orthogonality independent of κ(A), Householder reflections are the right answer — at the cost of a much heavier, less streamable datapath.
Every one of these is documented in docs/fixed_point.md with the derivation behind it.
Notes: Stating limits precisely is part of the deliverable — a numerical block whose failure mode is undocumented is not finished.

## Slide 26
IN SUMMARY
Three decisions carry the design
1
Modified, not Classical
Orthogonality degrades like u·κ(A) instead of u·κ(A)². At κ=10³ the hardware measures 102 LSB where CGS would give roughly 5×10⁵ — nothing usable.
2
One array, two operations
Normalisation and projection removal share vec_axpy, halving the DSP cost of the update path.
3
No divider, no square root
rsqrt_unit recovers ‖v‖ = m·(1/√m)·2ʰ from the same multiplier Newton–Raphson already uses.
Run it yourself
cd sim
make test # build, simulate, self-check
make regress # 23-configuration sweep
make test M=16 N=8 P=4 # any geometry
23/23
regression configurations pass
exact
match to the bit-accurate model
2P+1
multipliers, no divider
Notes: Close on the three decisions and the one-line way to reproduce every number in the deck.